## Slide 1
Methanol (CH3OH) is an attractive choice of fuel due to its large availability because it can be produced from renewable resources.
Microreactors have been employed for renewable fuel production because of enhanced mass transfer, better temperature control leading to improved heat transfer and larger surface-area-to-volume ratios 1.
Recently microreactors for hydrogen production have been employed to provide the on-line hydrogen source for polymer electrolyte membrane fuel cells (PEMFCs).
The catalytic steam reforming of methanol occurs with the CuO/ZnO/Al2O3 catalyst 2:
RESULTS
CONCLUSIONS
The modelling results have shown a good validation with experimental results.
The performance of the packed bed and coated wall reformer at a constant wall temperature was analogous, indicating that the average temperature of the catalyst bed in the packed bed microreactor and the average temperature of the catalyst layer in the coated wall microreactor are similar.
It was concluded that there were negligible internal and external mass transfer resistances, which agreed with the experimental results.
S. Hafeez, G. Manos, S. Al-Salem, E. Aristodemou and A. Constantinou, React. Chem. Eng., 2018, 3, 414-432.
J. Amphlett, K. Creber, J. Davis, R. Mann, B. Peppley and D. Stokes, Int. J. Hydrog. Energy, 1994, 19, 131-137.
M.-t. Lee, R. Greif, C. P. Grigoropoulos, H. G. Park and F. K. Hsu, J. Power Sources, 2007, 166, 194-201.
Figure 1. Packed bed and coated wall microreactors used for the modelling.
Figure 2. Comparison of coated wall and packed bed microreactors at different catalyst sizes and wall temperatures with experimental 3 results: (a) Tw=210 oC, S/M=1.1; (b) Tw=220 oC, S/M=1.1; (c) Tw=230 oC, S/M=1.1.
Packed Bed and Coated Wall Microreactors for Methanol Steam Reforming for Hydrogen Production
Sanaa Hafeez1, Elsa Aristodemou1, S.M. Al Salem2, George Manos3 and Achilleas Constantinou1,3
1. London South Bank University, London, UK 2. Kuwait Institute for Scientific Research, Kuwait 3. University College London, London, UK
Excerpt from the Proceedings of the 2020 COMSOL Conference
The mass balance equation for the species in the catalyst bed is given by:
(1)
The specific surface area of the pellets exposed to the fluids in the packed bed and can be expressed as:
(2) (3)
The mass transfer can be demonstrated as:
(4) (5)
(6) (7)
(8)
The mass balance inside the catalyst pellet is acquired by conducting a shell balance across a spherical shell:
(9)
210 oC
220 oC
230 oC
210 oC
220 oC
230 oC
Figure 3. (a) Concentration profiles of CH3OH within the catalyst particle at varying axial height of the packed bed microreactor. (b) Concentration profiles of CH3OH at the catalyst particle surface and the bulk fluid at varying axial height of the packed bed microreactor.
Figure 4. Molar variations of (a) CH3OH; and (b) H2; for varying catalyst thickness along the axial direction of the coated wall microreactor.
INTRODUCTION
COMPUTATIONAL METHODS
CONCLUSIONS